## Slide 1: MediSaver: An Epipen Alternative
Vikram Arun, Ben Katzman, Luke Ziolkowski

## Slide 2: Outline
Project Scope
Design Components
Design Specifications & Testing Results
Demonstration
Future Steps

## Slide 3: Project Scope
$4B auto-injector market dominated by Epi-Pen
Propose a more practical, safe, and efficient alternative to deliver Epinephrine in an emergency
Consistent and Reliable
Intramuscular Jet Injector

## Slide 4: Outline
Project Scope
Design Components
Design Specifications & Testing Results
Demonstration
Future Steps

## Slide 5: Parts List
3D printed pieces (PBA filament): $21.99, amazon.com
(1) Shell
(2) Button
(3) Plunger
(6) Guide
(7) Clip
(8) Cap
Purchased pieces:
(4) Everbilt® Zinc-Plated Compression Spring $3.72, homedepot.com
(5) BD® Syringe 27 Gauge, 1cc, 1/2" Needle $.90/needle, healthwarehouse.com
Left to right: (1) Shell, (2) Button, (3) Plunger, (4) Spring, (5) Syringe, (6) Guide, (7) Clip, (8) Cap
(2) (3) (4) (5) (6) (7) (8)
Notes: Fix labeling

## Slide 6: Full Assembly

## Slide 7: Outline
Project Scope
Design Components
Design Specifications & Testing Results
Demonstration
Future Steps

## Slide 8: Design Specifications
Physical
Usage
Biological
Structure
Miscellaneous

## Slide 9: Physical Design Specifications
Weight ( <1 kg)
Portability (<82 cm^3)
Width (< 2.54 cm)
Convenient to carry around
✅ 49.8 grams
✅ 76.2 cm^3
✅ 2.54 cm

## Slide 10: Usage Design Specifications
Preparation + Delivery Time
Invasiveness
Application site damage
Delivery Obstacles
Ease of Use
Can be used safely and easily in a multitude of scenarios
✅ Consistently below 10 seconds to inject
✅ 27 gauge needle
✅ Minimal Damage to Gel
✅ Can be applied with clothes on
✅ Easily administered by a 3rd party

## Slide 11: Biological Design Specifications
Onset of Absorption
Plasma Concentration over Time
Dosage Accuracy
Dosage Variability
Intramuscular Injection of Epinephrine is Biologically Sufficient
✅
✅
✅
✅ .3 and .15 mg versions

## Slide 12: Structural Design Specifications
Force of Activation
Fall Durability
Weight Durability
X Button is sensitive
✅ 2m drop test
✅ 400N
Resilient and Reliable

## Slide 13: Miscellaneous Design Specifications
Accident Prevention
Safety after Use
Cost to Produce
Repeatability
Longetivity
Trackability
Clear Instructions
✅ Cap piece to prevent accidental injection
X Needle cannot be retracted
✅ $26.61
X No cartridges, must be disposed of
✅ Durable
✅ Clip-on
✅ Comprehensive Label

## Slide 14: Instructions on Label

## Slide 15: Outline
Project Scope
Design Components
Design Specifications & Testing Results
Demonstration
Future Steps

## Slide 16: Demonstration

## Slide 17: Injection Proof

## Slide 18: Outline
Project Scope
Design Components
Design Specifications & Testing Results
Demonstration
Future Steps

## Slide 19: Future Goals
Improve the stability of the device
Variable needle lengths or injection pressures for children/adults
Clinical and In Vivo trials with Epinephrine
Explore casing methods to maintain temperature independence for medicant
Test different gauge needles with the same depth and needle length

## Slide 20: Acknowledgements
Dr. Klaesner
Darshit Mehta
Professor Widder
Washington University in St. Louis's School of Medicine -- Allergy, Immunology, and Pulmonary Medicine Department
  Dr. Horner
  Dr. Beigelman
  Dr. Kitcharoensakkul

## Slide 21: Thanks!
Questions?